# NXTDataLogger/NXJChartingLogger Logging Protocol Definitions
Kirk P. Thompson
lejos@mosen.net
6/16/2012

Defines message structure and usage for logging messages in (NXT-side) lejos.util.NXTDataLogger and (PC-side) lejos.pc.charting.LoggerProtocolManager.
# Description
The protocol defines a command signaling scheme used from the NXT via lejos.util.NXTDataLogger to the lejos.pc.charting.LoggerProtocolManager running on the PC.

LoggerProtocolManager is used by the NXJChartingLogger PC charting/logging client application for managing the flow of data through the i/o streams from the NXT and parsing and disseminating the data via an event model defined by lejos.pc.charting. LoggerListener.

The data is read in 4 byte chunks.
After ATN, 2 bytes are read. This is the command and command parameter.

All commands are sent after an ATN sequence for each command.

The initial default datatype on instantiation is set to DT_INTEGER on both the NXT and PC classes. Once a datatype is set, it is current until it is changed. This reduces overhead of signaling a datatype for each value being logged. The COMMAND_DATATYPE allows changing of the current datatype.
# ATTENTION (ATN) Sequence
The ATN sequence is used to signal the receiver on the PC (LoggerProtocolManager) that a command sequence is immediately forthcoming. It is a 4 byte package that is constructed using 2 well-defined ATN values followed by a random value. The sum of these values are XORed with 0xFF and this value is stored as the last byte.

This scheme is not a CRC but merely provides a very low probability that actual logged data could inadvertently represent an ATN package, which [to put it mildly] would mess with the state management mechanism of LoggerProtocolManager. Note that proper mathematical rigor has not been applied to prove this.

Byte index	Description	Value
0	ATN value 1: ATTENTION1	-1 (0xFF)
1	ATN value 2: ATTENTION2	-85 (0xAB)
2	Random/arbitrary byte value	Varies. The NXTDataLogger implementation uses an array of 5 pre-calculated random values whose elements are continuously cycled through to eliminate the cost of continually producing random values. Your implementation may differ.
3	check sum	sum of the elements [0-2] values XORed with 0xFF

# Command Structure
The protocol supports 5 commands. These commands are packed in a 2 byte array and sent to the PC immediately after an ATN request to be parsed by LoggerProtocolManager:

Structure:
Byte index	Description
0	Command ID. See 3.1.
1	Command parameter. Used for DATATYPE and SETHEADERS. Value ignored on other commands but 0xFF (-1) has been used as convention.

# Commands:
The ID representation in Java is:
    private static final byte ATTENTION1 = (byte)0xff;
    private static final byte ATTENTION2 = (byte)0xab;
    private static final byte COMMAND_DATATYPE = 1;
    // sub-commands of COMMAND_DATATYPE
    private static final byte DT_BOOLEAN = 0;
    private static final byte DT_BYTE = 1;
    private static final byte DT_SHORT = 2;
    private static final byte DT_INTEGER = 3;
    private static final byte DT_LONG = 4;
    private static final byte DT_FLOAT = 5;
    private static final byte DT_DOUBLE = 6;
    private static final byte DT_STRING = 7;
    private static final byte COMMAND_SETHEADERS = 2;
    private static final byte COMMAND_FLUSH = 3;
    private static final byte COMMAND_COMMENT = 4;
    private static final byte COMMAND_PASSTHROUGH = 5;

Each command must be preceded by the ATN sequence.

Commands:
# Command DATATYPE : Datatype Representation Semantics
Command	command value	parameter value	description
DATATYPE	1	0-7	Set the current datatype. See 3.2
SETHEADERS	2	0-255: number of columns/headers being set	Signal the number of column headers that are about to be sent. See 3.3
FLUSH	3	-1 (0xFF)	Instruct the protocol manager to send any remaining logged line (whole or partial) to listener. Used in EOF processing. See 3.4 / TODO verify functionality
COMMENT	4	-1 (0xFF)	Send a string comment. NXTDatalogger does this in the next called finishLine(). See 3.5
PASSTHROUGH	5	-1 (0xFF)	Send arbitrary length byte array to be handled by lejos.pc.charting. TunneledMessageManager. See 3.6
CHARTTYPE	6	1-4	Sets the chart type to display. See 3.7

The NXTDataLogger class uses DataOutputStream for encoding logged values except STRING and thus they are byte encoded using the semantics defined in the Java Language Specification (JLS) §22.2.

The DATATYPE command is used to specify the current datatype. This datatype is in effect until a subsequent DATATYPE command is used.

Datatypes overview:
- Little-Endian transmittal of byte encoded values.
- 4 byte boundaries force smaller datatypes to be encoded as an int:
  - Boolean: 0=false, 1=true
  - byte: same value
  - short: same value
- Comment String uses null (0x00) terminated US-ASCII string with 4 byte boundaries with null padding on last chunk if needed.

The first column [0] per logged data row must always be the timestamp column. The timestamp datatype is INTEGER and the value is the number of milliseconds since the session/connection started. The LoggerProtocolManager keeps track of the number of columns per row based on the defined headers sent via the SETHEADERS command (3.3).
# BOOLEAN: ID value =0
Sent as int (4 bytes).

Value of 0 represents false. Value of 1 represents true. The implementation used by NXJChartingLogger has Boolean values saved in the log file as strings “true” or “false” and plotted in the chart as 1 or 0, respectively.
# BYTE: ID value =1
Sent as int (4 bytes).
# SHORT: ID value =2
Sent as int (4 bytes).
# INTEGER: ID value =3
Sent as int (4 bytes).
# LONG: ID value =4
Sent as long (8 bytes).
# FLOAT: ID value =5
Sent as int (4 bytes) represented as per JLS §20.9.22.
# DOUBLE: ID value =6
Sent as long (8 bytes) represented as per JLS §20.10.21
# STRING: ID value =7
Sent as an array of bytes on even 4-byte boundaries. Characters are encoded as US-ASCII with single null termination. Residual boundary bytes on case of uneven boundary are set to 0 (null padding) to ensure even 4-byte boundary.

Note: In NXJChartingLogger, the STRING datatype is supported but any transmitted string value will be ignored. The string encoding mechanism is used for the COMMENT (3.5) and SETHEADERS (3.3) commands however.

# Command SETHEADERS
The SETHEADERS command is used to set the timestamp (domain axis) label and column/series headers (range axis). The parameter value for the SETHEADERS command is the number of columns + the timestamp “column” (which is used for the plot domain axis). The byte datatype maximum value is 255 so that means the protocol can provide 254 columns/series of data (the timestamp counts as 1) per row of logged data. It should be noted that the NXT Charting Logger will be severely dogged down if you do that.

The [element] position of each column definition is used by the charting component to define the series order per axis.

The NXT Charting Logger supports 4 independent axes on the same chart as the default. This is useful for plotting data with different magnitudes, etc. The column definition structure allows definition of target axis per series. This is the chart type CT_XY_TIMEDOMAIN (see 3.7)

The column definition strings are encoded and sent sequentially after the ATN sequence and SETHEADERS command using the same algorithm defined for the DATATYPE STRING (3.2.8).

The column definitions string format/structure for each column definition is:
[name]![Y or N to indicate if charted]![axis ID 1-4]

Chart type CT_XY_TIMEDOMAIN:
The first column [0] defined must always be the timestamp column in the format defined above. The timestamp datatype is INTEGER and the value is the number of milliseconds since the session/connection started. The label “milliseconds” is used by the NXTDataLogger implementation. This first column definition is used by the charting component as the domain label and is the first column in the datalog.

The subsequent column/series definitions are then sent as individual strings using the same format as the LoggerProtocolManager knows how many columns to parse based on the column count parameter value sent with the command.

For example, a log/chart with 2 series to be charted on axes #1 and #2 would be 3 strings sent after the ATN sequence and then the SETHEADERS command with a param value of 3:
milliseconds!Y!1
MySeries-1!Y!1
MySeries-2!Y!2

Any bang(!) character in the field/column name must be removed or parsing will fail in the NXT Charting Logger.

The LoggerProtocolManager keeps track of the number of columns per row based on the defined headers sent via the SETHEADERS command. If the header definitions need to be changed [e.g. add a column], the entire header definition must be re-sent with the changes. This action will spawn the current chart into a new window (if data is plotted in the chart), and resets and clears the chart in the NXT Data Logger window to use the new column header definitions. The data log will remain intact and will just get a new header row and logging commences with the new column definitions
# Command FLUSH
This command instructs LoggerProtocolManager to dump any partial datalog rows to the log and chart. This should done when the connection is about to be closed and it should be attempted to be done on i/o errors (after which the connection should be closed).
# Command COMMENT
In the NXT Charting Logger, comments are displayed on the chart as an event marker on the domain axis with the comment text as a label and the timestamp as the domain (X axis) value of the marker.

After the COMMENT command is sent, an INTEGER is sent that specifies the timestamp. The timestamp value is the number of milliseconds since the session/connection started. The comment text is then sent using the same algorithm defined for the DATATYPE STRING (3.2.8).
# Command PASSTHROUGH
Used for tunneling data to lejos.pc.charting.TunneledMessageManager via LoggerProtocolManager. See the document: NXTDataLogger/NXJChartingLogger Passthrough Protocol Definitions (NXTDataLogger Tunnel protocol.doc) for more details.

After the PASSTHROUGH command is sent, an INTEGER is sent that specifies how many bytes are in the pass-through message. The LoggerProtocolManager will poll this number of bytes from the i/o steam and pass this to the TunneledMessageManager which will in turn parse and process the message as per the Passthrough Protocol Definitions.

# Command CHARTTYPE
The CHARTTYPE command is used to signal which chart type to generate with supplied data. The default [if not specified] is 1. The different chart types require data items and SETHEADER to be a specific number/count per series.
## CT_XY_TIMEDOMAIN = 1
The initial (and default if not specified for backwards compatibility) NXJChartingLogger chart type. Displays data series on shared domain axis (ms timestamp). Up to 4 independent range axis can be displayed. One series defined per SETHEADER name.
## CT_XY_SCATTER = 2;
XY Scatter plot.
## CT_XYZ_BUBBLE = 3;
XY Bubble plot where Z is the diameter of the bubble in respect to the X data axis scale.
## CT_XY_POLAR = 4;
XY Polar plot where X is theta and Y is radius. NOT IMPLEMENTED as of 10/27/13